## Slide 1: A Shot at Visual Vulnerability Analysis
Ethan Kerzner1 Lee A. Butler 2 Charles Hansen1 Miriah Meyer1
1University of Utah
2US Army Research Laboratory

## Slide 2: Ballistic vulnerability analysis
Notes: In this design study we worked with analysts who are trying to improve the safety of military vehicles.
To do this, they must understand what happens when a vehicle gets shot.

## Slide 3
[Aberdeen Test Center]
Notes: One option is to actually shoot at the vehicles and see what happens.
This helps them identify what vehicle parts are likely to be damaged, and make recommendations to vehicle design based on those findings.
But this is expensive, so analysts use simulations in place of live fire testing.
They use these simulations enable engineers to find patterns and outliers in the vehicle vulnerability beyond what is fea
But understanding these simulations requires reasoning about spatial and non-spatial data.

## Slide 4
Physically-based
simulations
3D geometry
mobility
engine_system
transmission_system
valve
spark_plug
…
…
…
Functionality
Notes: This includes the target vehicle’s 3D geometry.
----
The physically-based simulations that compute the path of a shot through the vehicle.
----
And a hierarchical representation of the vehicle’s functionality which models damage to the vehicles capabilities.
---
In this design study, we created a tool to support the analysis of this multityped data.

## Slide 5: Challenges
Remote collaboration
Sensitive data
  Simplified test data
Large organization [SIBB10]
  Highly specialized individuals
  Decentralized authority
Notes: In addition to the multityped data, we were also challenged by the fact that we were working remotely.
Except for three short weeks working face-to-face with our target users, this entire project was conducted during weekly video conferencing sessions.
The challenges of working remotely were exacerbated by the sensitive nature of our collaborators data which could not be moved from their secure machines.
Except for the time we spent on site, all of the data we worked with were simplified test cases that did match the complexity of real data. All the figures in this talk and our paper show this simplified data.
Also our collaborators were members of a large organization which is characterized by highly specialized individuals who rely on teamwork to accomplish goals, often with no central authority over their workflows.

## Slide 6: Contributions
Data abstraction and task analysis for vulnerability analysis
Shotviewer, a prototype visualization tool
Strategy of view-design parallelism for multityped data
Recommendations for working with large organizations
Notes: We contribute the first thorough problem characterization, data abstraction, and task analysis for the domain of ballistic vulnerability.
Based on this analysis, we present a prototype visualization tool called Shotviewer that supports reasoning about combined spatial and non-spatial ballistic simulation data.
And we reflect on the process of designing shotviewer to find a strategy of view-design parallelism for working with multityped data.
The remainder of this talk will follow these contributions as an outline.

## Slide 7: Contributions
Data abstraction and task analysis for vulnerability analysis
Shotviewer, a prototype visualization tool
Strategy of view-design parallelism for multityped data
Recommendations for working with large organizations
Recommendations are marked with ℛ
Notes: The recommendations mentioned throughout the talk. They will be marked with this bold symbol.

## Slide 8: Multityped data and tasks
Collaborators, methods, data, and tasks
Notes: Before getting into the data and tasks of ballistic vulnerability analysis, we will introduce our collaborators and the methods we used to interface with them.

## Slide 9: Collaborators
Producers
Analysts
Consumers
Target users: three ballistic analysts
Other collaborators:
  Three engineers producing simulation inputs
  One evaluator consuming analysts’ results
Notes: Our target users were three ballistic vulnerability analysts, but in order to completely understand the relevant data and tasks we sampled other people in the organization.
In particular, we worked with three engineers who produce simulation inputs and one evaluator who consumers the analysts' results.

## Slide 10: Collaborators
Producers
Analysts
Consumers
Target users: three ballistic analysts
Other collaborators:
  Three engineers producing simulation inputs
  One evaluator consuming analysts’ results
ℛ1 Sample the relevant data pipeline
Notes: The individuals beyond our target users lead us to the first recommendation of working with a large organization: sample the relevant data pipeline to get a better understanding of the relevant data and tasks.

## Slide 11: Methods
Semi-structured interviews
Site visit:
  Visualization awareness workshops [KS11]
  Contextual inquiry [WFB96]
Vis awareness samples
Images: [JS91, MMH*13, KERC09, DGH03]
Notes: With all of our collaborators, we used unstructured interviews to build an initial understanding of their workflow.
We performed the most useful methods during our site visits.
We used visualization awareness workshops where we showed a variety of visualizations from research literature. These seminars were particularly effective at engaging our collaborators as it showed them the potential of visualization
This engagement was important for contextual inquiry where we shadowed analysts in their real work environment.
From these methods, we built the following data abstraction.

## Slide 12: Data abstraction
mobility
engine_system
transmission_system
valve_assembly
spark_plug
…
…
…
Shotline
Dependency graph
3D geometry
Notes: Input to ballistic simulations is a 3D geometry model. This model is divided into components which correspond to physical parts.
Some of these components appear in the vehicles dependency graph.
This directed acyclic graph represents the vehicles functionality in terms of its components.
Its leaves are components. Its internal nodes are systems. And its roots are capabilities.
Here, if the shot hits a component called the valve assembly, then that damage propagates up the dependency graph, damaging the engine system and the truck’s mobility.
The relationships between the shotlines, the geometry, and the dependency graph gets boiled down to a single quantitative value that represents damage to the truck’s mobility.

## Slide 13
mobility
engine_system
transmission_system
valve_assembly
spark_plug
…
…
…
Shotline
Dependency graph
3D geometry
Notes: Input to ballistic simulations is a 3D geometry model. This model is divided into components which correspond to physical parts.
Some of these components appear in the vehicles dependency graph.
This directed acyclic graph represents the vehicles functionality in terms of its components.
Its leaves are components. Its internal nodes are systems. And its roots are capabilities.
Here, if the shot hits a component called the valve assembly, then that damage propagates up the dependency graph, damaging the engine system and the truck’s mobility.
The relationships between the shotlines, the geometry, and the dependency graph gets boiled down to a single quantitative value that represents damage to the truck’s mobility.

## Slide 14
mobility
engine_system
transmission_system
valve_assembly
spark_plug
…
…
…
Shotline
Dependency graph
3D geometry
Notes: Input to ballistic simulations is a 3D geometry model. This model is divided into components which correspond to physical parts.
Some of these components appear in the vehicles dependency graph.
This directed acyclic graph represents the vehicles functionality in terms of its components.
Its leaves are components. Its internal nodes are systems. And its roots are capabilities.
Here, if the shot hits a component called the valve assembly, then that damage propagates up the dependency graph, damaging the engine system and the truck’s mobility.
The relationships between the shotlines, the geometry, and the dependency graph gets boiled down to a single quantitative value that represents damage to the truck’s mobility.

## Slide 15
mobility
engine_system
transmission_system
valve_assembly
spark_plug
…
…
…
Shotline
Dependency graph
3D geometry
Notes: Input to ballistic simulations is a 3D geometry model. This model is divided into components which correspond to physical parts.
Some of these components appear in the vehicles dependency graph.
This directed acyclic graph represents the vehicles functionality in terms of its components.
Its leaves are components. Its internal nodes are systems. And its roots are capabilities.
Here, if the shot hits a component called the valve assembly, then that damage propagates up the dependency graph, damaging the engine system and the truck’s mobility.
The relationships between the shotlines, the geometry, and the dependency graph gets boiled down to a single quantitative value that represents damage to the truck’s mobility.

## Slide 16: Simulation output
Notes: This single quantitative damage value then gets colormapped and displayed in a visualization like this one, called a cell plot.
Here, each cell represents a shot at the vehicle in the direction that we’re looking. Color encodes damage to the truck’s mobility and firepower system for each shot.

## Slide 17: Simulation output
*Not responsible for colormap
*
Notes: (Joke about the colormap.)
These cell plots are the primary output of the simulations. Analysts generate from 3 to 42 different cell plots for a vehicle with different trajectories around the vehicle.
Reasoning about vehicle vulnerability requires being able to explain the colors of this cell plot. For instance, what components are getting damaged that cause a set of cells to be red.
This is challenging because cell plots are ambiguous: they contain no information about why a cell is a certain color.

## Slide 18: Simulation output
Notes: This single quantitative damage value then gets colormapped and displayed in a visualization like this one, called a cell plot.
Here, each cell represents a shot at the vehicle in the direction that we’re looking. Color encodes damage to the truck’s mobility and firepower system for each shot.

## Slide 19: Simulation output
Notes: The data behind cell color is a mix of multityped data – the geometry, dependency graph, and physical simulations.
Analysts currently rely on text files to make sense of this data.
----
To give you a taste of these text files, there are log files which contain a text description of the physics simulations.
In our simplified test data one of these files was 2Gb in size.
----
Then there are the system dependency graphs, which are also represented as a text file.
----
And in order to view the 3D geometry, analysts must use yet another text file to perform a manual indirection from human-readable names into region id numbers for their CAD software.

## Slide 20: Task analysis
20
Understand a shot’s spatial context
Understand a shot’s degradation and damage
Understand a shot’s systemic impact
Notes: We identified the following three tasks as key parts of understanding the cause of cell color.
Essentially, analysts must reason about the multityped data including the spatial context of the shot, how the shot breaks apart and goes through the vehicle, and how the shot impacts the vehicles systems.
For instance, understanding what causes this group of red cells to be red can identify why this truck’s mobility system is vulnerable to some type of shot.
Analysts use this to explain trends in cell plots. We observed that analysts perform these tasks for two shotlines in parallel, and use the differences to explain outcomes.
For instance, here the differences between the red and white cell are used to explain this red group of cells.

## Slide 21: Shotviewer’s design
Methods, example usage, and validation
Notes: Now that we’ve outlined the data and task, we will look at the design of our prototype visualization system called Shotviewer.

## Slide 22: Parallel and participatory design
Sketches and low fidelity prototypes
Interactive
prototypes
Notes: We built prototypes by involving analysts in sketching prototypes on paper, often trying to come up with many possibilities at a time.
We then refined these sketches into data sketches and ultimately working prototypes.

## Slide 23: Parallel and participatory design
Sketches and low fidelity prototypes
Interactive
prototypes
ℛ2 Recognize test data is not real data
Notes: Throughout this process, we were forced to sketch and work with test data.
We found that it was particularly useful to get feedback on how the test data differed from real data.
For instance, in terms of its scale of features.

## Slide 24
ℛ3 Automate everything
ℛ4 Budget time for data transition
Notes: We tested prototypes during weekly video conferences like this one.
In order to streamline the installation process, both for demonstrations and for deploying our tool, we found it was useful to automate the entire process. This included building our tool and all of its dependencies.
When we moved on site, we also found that it was useful to budgeting time for transitioning to real data. This allowed us to maximize the short amount of face time with our target users.

## Slide 25: Example usage
Notes: The resulting prototype can be explained with example usage.

## Slide 26: Shotviewer
Notes: The result of this process is our prototype software called Shotviewer.
Shotviewer acts as a details-on-demand for existing visualizations. Think of it as explaining the color behind cell plots.
It uses three linked views to display information about the multityped data.

## Slide 27: Shot spatial context
35
Notes: The 3D geometry view enables us to place the shot components in the truck’s geometry.

## Slide 28: Shot degradation and damage
Notes: The shotline view then provides details about the shot.
This includes the shots mass and velocity as it was going through the vehicle.
It also displays information about the components which get damaged, which are marked by the red glyph.

## Slide 29: Shot systemic impact
Notes: Selecting the component in the shotline view also highlights it in the system view, where we can see that damage to the valve assembly damages the truck’s mobility as shown by the thick blue path.

## Slide 30: Shotviewer
Notes: The result of this process is our prototype software called Shotviewer.
Shotviewer acts as a details-on-demand for existing visualizations. Think of it as explaining the color behind cell plots.
It uses three linked views to display information about the multityped data.

## Slide 31: Shotviewer
See paper for validation:
  User feedback
  Case studies
Notes: The result of this process is our prototype software called Shotviewer.
Shotviewer acts as a details-on-demand for existing visualizations. Think of it as explaining the color behind cell plots.
It uses three linked views to display information about the multityped data.

## Slide 32: View-design parallelism
Problem and strategy
Notes: We call this divide-and-conquer strategy view-design parallelism.

## Slide 33: View-design parallelism
Sep
Jan
May
Sep
Initial understanding
Notes: It can best be explained by looking at a timeline of our work.
We were initially overwhelmed with the multityped data which had an uncountable number of design possibilities.
Also, our collaborators wanted to see all of their data immediately--making it hard to focus them on a specific type.
At this initial point we were stuck and frustrated.
Rather than trying to work with all three data types at once….

## Slide 34: View-design parallelism
Sep
Jan
May
Sep
Initial understanding
Shotline view
Notes: We focused explicitly on just one data type – the simulation results. And iterated toward an implemented prototype.
Getting to a tangible prototype, even if just for one data type, injected new life into the project as it excited our collaborators.
While developing the Shotline View we stalled for several reason, such as waiting for data, parsers or feedback.
Because of these stalls, we were able to overlap design activities for a second view with the first one.

## Slide 35: View-design parallelism
Sep
Jan
May
Sep
Initial understanding
Shotline view
System view
Two view prototype
Notes: In parallel we developed the system view.
This was particularly effective because the variety of activities at any one time kept us from getting exhausted.
Ultimately, we combined the system view and shotline view into a prototype.

## Slide 36: View-design parallelism
Sep
Jan
May
Sep
Initial understanding
Shotline view
System view
Two view prototype
Geometry view
Final prototype
Notes: Concurrently, we were developing the geometry view.
And this was later combined into the final three view system which was our final prototype.
The key idea of view design parallelism is to build views for a visualization in a parallel and staggered fashion.

## Slide 37: View-design parallelism
Sep
Jan
May
Sep
Initial understanding
Shotline view
System view
Two view prototype
Geometry view
Final prototype
Build linked views in order of:
  Availability
  Usefulness
  Impact
  Time
Notes: When the opportunity to create a new view arises, we advocate selecting a view whose data is available, and that we can design quickly with a large impact.
We believe it is particularly effective when working with multityped data, though future work is needed to validate it beyond this design study.

## Slide 38: Conclusion
Data abstraction and task analysis for vulnerability analysis
Shotviewer, a prototype visualization tool
Strategy of view-design parallelism for multityped data
Recommendations for working with large organizations
Notes: In conclusion, we have contributed the first thorough problem characterization, data abstraction, and task analysis for the domain of ballistic vulnerability analysis.
We presented a prototype visualization tool called Shotviewer that supports reasoning about combined spatial and non-spatial ballistic simulation data.
We also reflected on the process of designing shotviewer to find a strategy of view-design parallelism for working with multityped data.

## Slide 39: A Shot at Visual Vulnerability Analysis
http://www.ethankerzner.com/projects/shotviewer
kerzner@sci.utah.edu

## Slide 40: Cell plot legend

## Slide 41: Cell plot legend